## Slide 1
Planning-oriented Autonomous Driving
Presented by Camilo Martínez
Seminar AI4AD
By Yihan Hu* Jiazhi Yang* Li Chen*+ Keyu Li*
CVPR 2023
Advances in AI for Autonomous Driving
1

## Slide 2
Table of Contents
I
II
III
IV
V
II
III
IV
V
I
II
III
IV
V
I
1. Motivation
2. Methodology
3. Experiment & Results
4. Limitations
5. Conclusions
2

## Slide 3
Motivation
Standalone Models
1
They bare the risk of
information loss
error accumulation
feature misalignment
End-to-End Systems
3
They unite perception, prediction and planning as a whole.
Multi-Task Learning
2
May cause undesirable
“negative transfer”.
3
Notes: Onboard chip resources allow. Simplifies R&D difficulty.
Isolated Optimization Objective per task
Object Detection: mAP
Motion Prediction: minFDE

## Slide 4
Standalone Models
1
They bare the risk of
information loss
error accumulation
feature misalignment
End-to-End Systems
3
They unite perception, prediction and planning as a whole.
Multi-Task Learning
2
May cause undesirable
“negative transfer”.
Motivation
4
Notes: Shared feature for multiple tasks
Easily extended to more tasks, compute-efficient
Lack of tasks’ coordination

## Slide 5
Standalone Models
1
They bare the risk of
information loss
error accumulation
feature misalignment
End-to-End Systems
3
They unite perception, prediction and planning as a whole.
Multi-Task Learning
2
May cause undesirable
“negative transfer”.
Motivation
5
Notes: Direct policy learning from sensor inputs, bypassing intermediate tasks
Simple design with good performance in the simulator
Deficient in interpretability
The choice and priority of preceding tasks should be determined in favor of planning

## Slide 6
Perception
Which Tasks?
Prediction
Object Detection
Object Tracking
Semantic Segmentation
Online Mapping
Depth Estimation
Traffic light/sign Detection
…
Motion Forecasting
Intention Prediction
Occupancy Prediction
…
Upper-level
Medium-level
Low-level
AD Tasks
Safe Planning
Track Agents Behavior
Map (lane) Guidance
Environment Interaction
Find free space
6

## Slide 7
Coordinate all task towards
safe planning
Unify full-stack AD tasks
GOALS
Planning
Prediction
Perception
Object Detection, Object Tracking, Online Mapping
Motion Forecasting, Occupancy Prediction, Find free space
Track Agents Behavior
Guide with lanes
Environment Interaction
The UniAD
7

## Slide 8
DESIGN | APPROACH | WORK | PERCEPTION |  |  | PREDICTION |  | PLAN
 |  |  | Detect | Track | Map | Motion | Occup. | 
Multi-task Framework | NMP | CVPR 2019 | ✔ |  |  | ✔ |  | ✔
 | NEAT | ICCV 2021 |  |  | ✔ |  |  | ✔
 | BEVerse | 2022 | ✔ |  | ✔ |  | ✔ | 
Explicit Design | PnPNet | CVPR 2020 | ✔ | ✔ |  | ✔ |  | 
 | ViP3D | CVPR 2023 | ✔ | ✔ |  | ✔ |  | 
 | P3 | ECCV 2020 |  |  |  |  | ✔ | ✔
 | MP3 | CVPR 2021 |  |  | ✔ |  | ✔ | ✔
 | ST-P3 | ECCV 2022 |  |  | ✔ |  | ✔ | ✔
 | LAV | CVPR 2022 | ✔ |  | ✔ | ✔ |  | ✔
Vanilla Solution | [7, 9, 45, 54] | 2020-2022 |  |  |  |  |  | ✔
Planning Oriented Design | UniAD | CVPR 2023 | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
8
Tasks Comparison & Taxonomy

## Slide 9
Table of Contents
I
II
III
IV
V
II
III
IV
V
I
II
III
IV
V
I
1. Motivation
2. Methodology
3. Experiment & Results
4. Limitations
5. Conclusions
9

## Slide 10
The UniAD Pipeline
Track agents across time
Segment map elements
Scene-level representation
Planned final trajectory
Avoid collision
Tasks coordinated with queries
Interactions modelled by attention
Unified Query
Transformer-based
Prediction
Perception
Planning
Predict long-term trajectory
10

## Slide 11
The UniAD Pipeline
Prediction
Perception
Planning
BEV Encoder – BEVFormer (ECCV 2022)
INPUT
A sequence of multi-camera images are transformed into a unified bird’s-eye-view (BEV) feature by BEVFormer.
ADVANTAGES
Strong BEV encoder with effective spatial and temporal feature extraction.
Not really part of the main pipeline of UniAD, that is, it’s not confined to this one specifically.
11
Notes: One can utilize other alternatives to extract richer BEV representations with long-term temporal fusion or multi-modality fusion.

## Slide 12
The UniAD Pipeline
Prediction
Perception
Planning
MOTR (ECCV 2022)
Panoptic SegFormer (CVPR 2022)
End-to-end Multiple Object Tracking without post-association.
Road elements are represented as map queries.
12
Notes: One can utilize other alternatives to extract richer BEV representations with long-term temporal fusion or multi-modality fusion.

## Slide 13
The UniAD Pipeline
Prediction
Perception
Planning
MOTR (ECCV 2022)
Panoptic SegFormer (CVPR 2022)
End-to-end Multiple Object Tracking without post-association
Road elements are represented as map queries.
agents’ information
Track queries ↔
Detects and track agents
Detection queries are responsible for detecting newborn agents
layers valid agents
+
Lanes, dividers, crossings as things
Drivable area as stuff
layers updated last layer
13
Notes: At each time step, initialized detection queries are responsible for detecting newborn agents that are perceived for the first time, while track queries keep modeling those agents detected in previous frames.
Both detection queries and track queries capture the agent abstractions by attending to BEV feature B.
Track queries at the current frame interact with previously recorded ones in a self-attention module to aggregate temporal information, until the corresponding agents disappear completely (untracked in a certain time period).

## Slide 14
The UniAD Pipeline
Prediction
Perception
Planning
Proposed in UniAD
NON-LINEAR OPTIMIZATION
Adjust ground-truth trajectory based on upstream prediction.
Diverse relation modelings via attention mechanism:
  agent-agent, agent-map, agent-goal
14
Notes: It is composed of N layers, and each layer captures three types of interactions: agent-agent, agent-map and agent-goal point

## Slide 15
The UniAD Pipeline
Prediction
Perception
Planning
Proposed in UniAD
TrackFormer
MapFormer
MotionFormer
layers
Top-k possible trajectories
Multi-agent trajectories in the frame with a single forward pass
Ego-vehicle query interacts with other agents (future dynamics)
More formally,
  indexes the agent
  indexes the modality of trajectories (6)
  is the length of prediction horizon (12)
15
Notes: Dynamic agents Q_A and static map queries Q_M
Scene-centric manner.

## Slide 16
The UniAD Pipeline
Prediction
Perception
Planning
Proposed in UniAD
For a motion query ,
: multi-head cross attention.
: multi-head self-attention.
agent-agent, agent-map
agent-goal
MLP
Last layer output
To focus on the intended position/goal:
: predicted trajectory of previous layer.
16
Notes: Q_i,k (omitting subscripts i, k for simplicity), its interactions between other agents Q_A or map elements Q_M could be formulated as shown.
Through deformable attention, the predicted trajectory is further refined as aware of the endpoint surroundings.

## Slide 17
The UniAD Pipeline
Prediction
Perception
Planning
Proposed in UniAD
Motion Queries:
Scene-level anchors
Agent-level anchors
Current location
Predicted goal point
: sinusoidal positional encoding
Predicted endpoint optimized layer-by-layer in a coarse-to-fine fashion.
17
Notes: Scene-level anchors are prior movement statistics in a global view.
Agent-level anchor is the possible intention in a local view.

## Slide 18
The UniAD Pipeline
Prediction
Perception
Planning
Proposed in UniAD
Tackle prediction uncertainty
  denotes the ground-truth
  denotes the smoothed trajectory
  is generated by multiple shooting
  is the kinematic function set: jerk, curvature, curvature rate, acceleration and lateral acceleration
Imperfect detection
Instead, make them physically feasible given an imprecise starting point predicted by the upstream module:
Ground-truth waypoints
Unrealistic trajectories
Large curvature
Large acceleration
regression
18
Notes: The cost function regularizes the target trajectory to obey kinematic constraints.
This target trajectory optimization is only conducted in training and does not affect inference.

## Slide 19
The UniAD Pipeline
Prediction
Perception
Planning
Predict occupancy as attention mask
Encode agent-wise knowledge into the scene representation
Scene-level semantics
Agent-level semantics
Dense scene features ↔ agent-level (attention module)
Instance-wise occupancy via matrix multiplication:
agent-level features dense scene-features
sequential blocks, with from MotionFormer
High-computational cost
Agent features
OccFormer
State (dense feature)
Proposed in UniAD
Occupancy prediction
19
Notes: Occupancy grid map is a discretized BEV representation where each cell holds a belief indicating whether it is occupied, and the occupancy prediction task is to discover how the grid map changes in the future.
Each block takes the rich agent features G^t and the state F from the previous layer, and generates F^t considering both instance- and scene-level information.

## Slide 20
The UniAD Pipeline
Prediction
Perception
Planning
Agent features
OccFormer
State (dense feature)
Agent features contain dynamics and spatial priors via max-pooling motion queries from MotionFormer:
Then, early-fusion via a temporal-specific MLP:
  : upstream track query
  : current position embedding
  : concatenation
State (dense feature) is the BEV feature ¼ downscaled
Proposed in UniAD
20
Notes: Q_X is obtained by max-pooling from the modality dimension K

## Slide 21
The UniAD Pipeline
Prediction
Perception
Planning
Dense feature as queries
Instance-level features as keys and values to update the dense feature over time
Pixel-level interaction
Scene
Agent-level understanding
is obtained by multiplying with
is upsampled to ¼ the size of B and add as residual connection
Proposed in UniAD
21
Notes: Unify scene and agent-level interaction when predicting future occupancy
Restrict each pixel to only look at the agent occupying it at timestep t

## Slide 22
The UniAD Pipeline
Prediction
Perception
Planning
It represents the occupancy with each agent’s identity preserved
Original size of BEV feature B
is upsampled to
Update the coarse mask again,
Finally, the instance-level occupancy at time is
Instance-level occupancy
Proposed in UniAD
22
Notes: Represents the occupancy with each agent’s identity identified
It could be simply via matrix multiplication

## Slide 23
The UniAD Pipeline
Prediction
Perception
Planning
Ego-vehicle query consistently passed through TrackFormer, MotionFormer, and now Planner.
Planning
Proposed in UniAD
turn left
turn right
forward
3 learnable embeddings
(command embeddings)
+
“plan query”
↕
BEV Features B
attend
Avoid collisions through Newton’s method in inference
: original planning prediction
optimized planning
: generated by multiple shooting
: cost function to minimize
binary occupancy map from OccFormer
23
Notes: From the MotionFormer, the ego-vehicle already has multimodal intentions. Now we equip it with command embeddings to form a “plan query”.
We attend to BEV features to make it aware of surroundings and decode it to future waypoints tau.

## Slide 24
The UniAD Pipeline
Prediction
Perception
Planning
Unified Query
Transformer-based
24
Notes: One can utilize other alternatives to extract richer BEV representations with long-term temporal fusion or multi-modality fusion.

## Slide 25
How to train it?
Two-phase training
Perception stage + End-to-end stage
The stabilized perception capability helps the end-to-end stage converge faster
Tracking and Mapping modules
6 epochs
End-to-end training
20 epochs
Shared matching (Bipartite Matching Algorithm)
Inspired by DETR (DEtection TRansformer), which matches predictions to ground truth entities minimizing a cost function
Consistent learning of agent identities
Converges faster
25
From: https://www.youtube.com/watch?v=GdEVfcLYpPc
Notes: Matching results of tracking reused in motion and occupancy

## Slide 26
Table of Contents
I
II
III
IV
V
II
III
IV
V
I
II
III
IV
V
I
1. Motivation
2. Methodology
3. Experiment & Results
4. Limitations
5. Conclusions
26

## Slide 27
Ablation Results
01
Tasks benefit each other and contribute to safe planning
02
ID. 4-6: Track & Map → Motion
ID. 7-9: Motion ↔ Occupancy
ID. 10-12: Motion & Occupancy → Planning
03
The two perception sub-tasks greatly help motion forecasting, and prediction performance
04
UniAD outperforms naïve MTL solution
27
Evaluation on nuScenes
Notes: ID0 is the naive MTL implementation

## Slide 28
Ablation Results
All components contribute to the ultimate performance
Design of the MotionFormer
Rotated scene-level anchors
Agent-goal interaction
Ego-vehicle Query
Non-Linear Optimization
28

## Slide 29
Ablation Results
Cross-attention with masks and the reuse of mask feature helps improve the prediction
Design of the OccFormer
Cross- and Attention mask (Pixel-level interaction)
Re-use of Mask feature (Instance-level occupancy)
Not all metrics show best performance…
29
Notes: Reusing the mask feature M^t instead of the agent feature G^t to acquire the occupancy feature further enhances performance.

## Slide 30
Ablation Results
Results demonstrate the necessity of each preceding task
Design of the Planner
Attending to BEV feature
Collision Loss
Optimization strategy with Occupancy
Same as in OccFormer, not all metrics improve
30

## Slide 31
Results: Planning
01
UniAD achieves the lowest L2 error and collision rate in all time intervals
02
UniAD outperforms LiDAR-based methods in all investigated metrics
LiDAR-based
camera-based
31

## Slide 32
Results: Other tasks
Multi-Object Tracking
Motion Forecasting
Online Mapping
Occupancy Prediction
SOTA performance on almost all investigated tasks
32

## Slide 33
Qualitative Results
Obstacles avoidance visualization
The ego vehicle is changing lanes attentively to avoid an obstacle.
33
Notes: In these two scenarios, the ego vehicle is changing lanes attentively to avoid the obstacle vehicle. From the attention mask, we can observe that our method focuses on the obstacles as well as the road in the front and back

## Slide 34
Qualitative Results
Visualization for planning recovering from perception failures
Inaccurate results occur in prior modules while the later tasks could still recover.
34
Notes: In these two scenarios, the ego vehicle is changing lanes attentively to avoid the obstacle vehicle. From the attention mask, we can observe that our method focuses on the obstacles as well as the road in the front and back

## Slide 35
Table of Contents
I
II
III
IV
V
II
III
IV
V
I
II
III
IV
V
I
1. Motivation
2. Methodology
3. Experiment & Results
4. Limitations
5. Conclusions
35

## Slide 36
Limitations
Long-tail scenario
A large trailer with a white container occupies the entire road.
36
Notes: We can observe that our tracking module fails to detect the accurate size of the front trailer and heading angles of vehicles beside the road.

## Slide 37
Limitations
Over-cautious planner
Incoming vehicle in a narrow street in a dark environment.
37
Notes: In this case, the planner is over-cautious about the incoming vehicle in the narrow street. The dark environment is one critical type of long-tail scenarios in autonomous driving. Applying smaller collision loss weight and more regulation regarding the boundary might mitigate the problem

## Slide 38
W
S
O
T
Unified end-to-end framework
Planning-oriented design
Query-based task coordination
State-of-the-Art results
STRENGTH
Extensive computational power
Temporal history training
Limited scalability
WEAKNESS
Curation for a lightweight deployment
Integration & embedding of new tasks
(depth estimation, behaviour prediction)
OPPORTUNITY
Performance in rare/dark scenarios
Simpler/more lightweight methods
LiDAR-based methods
THREAT
Limitations: SWOT Analysis
38

## Slide 39
Table of Contents
I
II
III
IV
V
II
III
IV
V
I
II
III
IV
V
I
1. Motivation
2. Methodology
3. Experiment & Results
4. Limitations
5. Conclusions
39

## Slide 40
Integrates perception, prediction, and planning together, reducing error propagation compared to modular approaches
Unified Query design: Queries as interfaces to connect and coordinate all tasks in an interpretable fashion
State-of-the-art (SOTA) Performance with vision-only input
First Step towards Autonomous Driving Foundational Models
Conclusions – Authors’ View
UniAD
40

## Slide 41
Integrates perception, prediction, and planning together, reducing error propagation compared to modular approaches
Unified Query design: Queries as interfaces to connect and coordinate all tasks in an interpretable fashion
State-of-the-art (SOTA) Performance with vision-only input
First Step towards Autonomous Driving Foundational Models
UniAD
1
Conclusions – Authors’ View
41

## Slide 42
Integrates perception, prediction, and planning together, reducing error propagation compared to modular approaches
Unified Query design: Queries as interfaces to connect and coordinate all tasks in an interpretable fashion
State-of-the-art (SOTA) Performance with vision-only input
First Step towards Autonomous Driving Foundational Models
2
UniAD
Conclusions – Authors’ View
42

## Slide 43
Integrates perception, prediction, and planning together, reducing error propagation compared to modular approaches
Unified Query design: Queries as interfaces to connect and coordinate all tasks in an interpretable fashion
State-of-the-art (SOTA) Performance with vision-only input
First Step towards Autonomous Driving Foundational Models
3
UniAD
Conclusions – Authors’ View
43

## Slide 44
Integrates perception, prediction, and planning together, reducing error propagation compared to modular approaches
Unified Query design: Queries as interfaces to connect and coordinate all tasks in an interpretable fashion
State-of-the-art (SOTA) Performance with vision-only input
First Step towards Autonomous Driving Foundational Models
4
UniAD
Conclusions – Authors’ View
44

## Slide 45
Some Ablation Results are not conclusive, i.e., not all metrics are improving w.r.t features
Unified Query design: Queries as interfaces to connect and coordinate all tasks in an interpretable fashion
Some Design choices seem too abstract
State-of-the-art (SOTA) Performance with vision-only input
First Step towards Autonomous Driving Foundational Models
Much to learn we still have
Conclusions – My View
UniAD
45
Better comparison against LiDAR needed

## Slide 46
Thank you for your attention
Time for questions!
46

## Slide 47
  Carion, N., F. Massa, G. Synnaeve, N. Usunier, A. Kirillov, and S. Zagoruyko. End-to-End Object Detection with Transformers, 2020. arXiv: 2005.12872 [cs.CV]. https://arxiv.org/abs/2005.12872.
  Chen, L., P. Wu, K. Chitta, B. Jaeger, A. Geiger, and H. Li. “End-to-end Autonomous Driving: Challenges and Frontiers.” IEEE Transactions on Pattern Analysis and Machine Intelligence, 2024.
  Hu, Y. [CVPR2023 Award Candidate] UniAD: Planning-oriented Autonomous Driving. YouTube Video. Candidate Award Talk, available at https://www.youtube.com/watch?v=R4iuq3zDBL4, 2023.
  Hu, Y. CVPR23 Plenary Talk — [Best Paper] UniAD: Planning-oriented Autonomous Driving. YouTube Video. Plenary talk at CVPR 2023, available at https://www.youtube.com/watch?v=cyrxJJ_nnaQ, 2023.
  Hu, Y., J. Yang, L. Chen, K. Li, C. Sima, X. Zhu, S. Chai, et al. Planning-oriented Autonomous Driving, 2023. arXiv: 2212.10156 [cs.CV]. https://arxiv.org/abs/2212.10156.
  Li, Z., W. Wang, H. Li, E. Xie, C. Sima, T. Lu, Q. Yu, and J. Dai. BEVFormer: Learning Bird’s-Eye-View Representation from Multi-Camera Images via Spatiotemporal Transformers, 2022. arXiv: 2203.17270 [cs.CV]. https://arxiv.org/abs/2203.17270.
  Li, Z., W. Wang, E. Xie, Z. Yu, A. Anandkumar, J. M. Alvarez, P. Luo, and T. Lu. Panoptic SegFormer: Delving Deeper into Panoptic Segmentation with Transformers, 2022. arXiv: 2109.03814 [cs.CV]. https://arxiv.org/abs/2109.03814.
  Zeng, F., B. Dong, Y. Zhang, T. Wang, X. Zhang, and Y. Wei. MOTR: End-to-End Multiple-Object Tracking with Transformer, 2022. arXiv: 2105.03247 [cs.CV]. https://arxiv.org/abs/2105.03247.
  All illustrations and tables taken from the original paper: Planning-oriented Autonomous Driving (including Supplementary Material) by Hu, Y., J. Yang, L. Chen, K. Li, C. Sima, X. Zhu, S. Chai, et al., unless specified otherwise. The references listed on the tables have the enumeration from the original paper.
References
47